## Slide 1
Session 5 Deploying
TAPI-Based
Solutions
David Janson
Microsoft® Corp.

## Slide 2: Agenda
Client/Server Telephony
H.323
IP Multicast Conferencing

## Slide 3: Traditional TAPI Architecture
Telephony Service
Unimodem
H.323
TAPI 2.x Application
TAPI 3.0 Application
OEM TSP
NIC

## Slide 4: Client/Server Architecture
Client
Server
Telephony Service
OEM TSP
TAPI Application
Other TSP
Telephony Service
TAPI Application
RemoteSP
NIC
NIC
Other TSP

## Slide 5: Telephony Server Setup
NT 4.0 Server (SP6a) or Windows 2000 Server
TCP/IP
Install OEM TSP
  Make sure TSP works on Server
  Work with OEM
Create “Server” user domain acct
Enable Telephony Server
Set individual line permissions

## Slide 6: Server Setup – create user
create a domain user for the Telephony Server to run under
This user account must be in a domain trusted by clients
Recommended that it is in the same domain as the client user accounts
Recommended that it is named something obvious like “TAPI” or “Telephony”

## Slide 7: Enable NT 4.0 Telephony Server
TCMSetup /s domain/user password
TCMSetup.exe is installed with SP6a
/q switch available for quiet mode. For automatic ISV setup

## Slide 8: Enable Windows 2000 Telephony Server
MMC – Computer Management
  “Start” “Programs” “Administrative Tools” “Computer Management”

## Slide 9: Enable Windows 2000 Telephony Server (cont)
Select “Telephony” then “Action” “Properties”

## Slide 10: NT 4.0 Line Permissions
Run TCMApp.exe
Notes: Discuss “User” “Add” and giving individual users permissions

## Slide 11: Windows 2000 permissions
Still in Computer Management
Select a line and then:
  “Action” “Edit Users”

## Slide 12: Client Setup
NT 4.0 (SP6a), Windows 9x, Windows 2000
TCP/IP
Login via Windows NT user domain account
Windows 9x network settings
  Client for Microsoft Networks
  Enable "File and Print Sharing“
  Use “User-Level Access Control"
Windows 95
  “TAPI 2.1 for Windows 95” add-on needed
  ftp://ftp.microsoft.com/developr/tapi/tapi2195.zip
“tcmsetup /c servername”
  Again, /q switch available. Perfect for SMS.

## Slide 13: How remotesp.tsp works
Client
Server
Telephony Service
OEM TSP
Telephony Service
TAPI Application
RemoteSP
NIC
NIC
RPC over TCP/IP
RPC over TCP/IP

## Slide 14: How remotesp.tsp works, Step by Step
TAPI application on client starts TAPI
TAPI loads remotesp.tsp
Remotesp.tsp initiates RPC over TCP/IP connection to Server
Server validates user
Server makes a “Reverse” RPC connection back to client
Server assigns lines and completes first remotesp.tsp RPC connection

## Slide 15: Troubleshooting
You know it works when TAPI applications on the client can see their assigned line devices.
Problems:
  Basic Setup
  Networking
  Security
  Client Context

## Slide 16: Problem 1: Basic Setup
Most people don’t have trouble with basic setup. Follow the step by step directions.
The exception is environments that aren’t already using Windows NT domains.

## Slide 17: Problem 2: Networking
Can the client “ping” the server?
  Do normal networking troubleshooting
  RAS will change the route table.
Can the server “ping” the client?
  Don’t put the Telephony Server behind a firewall that prevents it from being able to ping the client.

## Slide 18: Problem 3: Security
Can the client “net view” the server?
  The server machine account needs to be in a domain that trusts the client user accounts
Can the server “net view” the client?
  Log in interactively using the “Telephony” user account
  This situation exists because of the “Reverse” RPC connection
  This is why the Telephony Server domain user account must be in a domain trusted by client machines

## Slide 19: Problem 4: Client Context
What user context started the Telephony Service on the Client?
  Remotesp.tsp only asks the Telephony Server for lines when started.
  If the Telephony Service is started before the interactive user logs in, then remotesp.tsp has already asked Telephony Server for lines and probably been denied.

## Slide 20: Problem 4: RAS example
RAS is installed on a client
  RAS is “autostart” by default
  RAS is configured to run under the “Local System” account
  When RAS starts, it starts TAPI
  TAPI initializes remotesp.tsp
  Remotesp.tsp asks the Telephony Server for line devices
  Telephony Server denies the client machines “Local System” any line devices
User now logs in and doesn’t see line devices.

## Slide 21: Problem 4: More examples
Fax Servers
Other TAPI based services
User A logs in, starts TAPI application, logs out, User B logs in
  The Telephony Service may take a short time to shutdown
Modem based applications are the most common examples

## Slide 22: Problem 4: Solutions
After logging in, check if the Telephony Service is started before starting any TAPI applications.
Solutions are on a case by case basis:
  Remove modems if possible
  Reconfigure RAS to “manual” start

## Slide 23: Note: WAN Clients
If remote.tsp can’t find server when it first starts, it will keep trying every 2 minutes. This allows for WAN clients to use the Telephony Server.

## Slide 24: Agenda
Client/Server Telephony
H.323
IP Multicast Conferencing

## Slide 25: H.323 – Point to Point
Destination
Telephony Service
Phone Dialer
H.323 TSP/MSP
Source
Telephony Service
Phone Dialer
ILS
Register
IP
Lookup
IP
H.323 TSP/MSP
TCP/IP

## Slide 26: H.323 Server configuration
Windows 2000 H.323 is point to point, so no servers
Phone Dialer can use the Internet Locator Service (ILS) Service
  Can be used to locate users running Phone Dialer
  ILS is a real-time server component of the Active Directory
  This is specific to Phone Dialer
  Setup of ILS covered later

## Slide 27: H.323 Workstation setup
Full Duplex audio
  This is the only “requirement”
  Can be verified by playing and recording simultaneously.
Beware of Acoustic Echo
  Use audio headsets
  Echo-canceling microphones
  Adjust volume
Install “Windows 2000” supported camera

## Slide 28: Use Phone Dialer to verify
Run Phone dialer on “Destination” to enable incoming calls
Make a call from “Source” with Phone Dialer
  Use TCP/IP address
  Use machine name
Phone Dialer can use both H.323 and IP Multicast Conferencing.

## Slide 29: Agenda
Client/Server Telephony
H.323
IP Multicast Conferencing

## Slide 30: How MCast works
Conf Creator
Telephony Service
Phone Dialer
MCast
ILS
Conf Member
Telephony Service
Phone Dialer
MCast
Conf Member
Telephony Service
Phone Dialer
MCast
Conf Member
Create Conference
Join Conference
Multicast TCP/IP

## Slide 31: Prerequisites
IP Multicast Conferencing needs several non-TAPI components
  TCP/IP multicast
  Active Directory
  Internet Locator Server (ILS)
  MADCAP
Follow “step by step” directions and it’s pretty easy

## Slide 32: Network Backbone
Must be TCP/IP Multicast capable
Test using MCAST.EXE on both multicast sender and multicast receiver.
  MCAST /SEND /INTF:172.31.253.55 /GRPS:230.1.1.1 /INTVL:1000 /NUMPKTS:3600
  MCAST /RECV /INTF:172.17.100.98 /GRPS:230.1.1.1
Routers may need to be configured.
  See your router vendor

## Slide 33: More Networking
This work may already be done if you have previously used a multi-cast application such as Windows Media Technologies (previously called NetShow)
Many routers on the Internet are not configured for multicast

## Slide 34: Setting up the Servers
Active Directory
  Part of setting up a Windows 2000 domain.
Site Server ILS Service
  Conferences are published here
  Conference members, multicast address, conference encryption key
MADCAP
  Similar to DHCP, but used to allocate Multicast addresses

## Slide 35: Site Server ILS Service
Needs Windows 2000 Server with Internet Information Server (IIS) installed
To install the Site Server ILS Service:
  Control Panel, "Add/Remove Programs"
  "Add/Remove Windows Components"
  "Networking Services"
  Click "Details"
  Check "Site Server ILS Services“
Use ILSCFG.EXE to publish in Active Directory

## Slide 36: Setting up MADCAP
Installed as part of DHCP
  Control Panel, "Add/Remove Programs"
  "Add/Remove Windows Components"
  "Networking Services"
  Click "Details"
  Check "Dynamic Host Configuration Protocol (DHCP)"

## Slide 37: Multicast Scopes
Multicast Scopes are used to specify the duration and availability of multicast “group” IP addresses
  MMC "Computer Management" again
  "Server Applications and Services"
  “Action“, "New Multicast Scope"

## Slide 38: Advice for Scopes
Make scopes useful.
Give options (1day, 5day, 10day, etc)
Make names descriptive! End-users creating conferences have to select a scope.
Time to Live (TTL) is number of hops to receiver. Use 255

## Slide 39: Setting up the Workstation
Audio and Video the same as H.323
Phone dialer “just works” if:
  Workstation is part of a Windows 2000 domain
  User is logged onto a Windows 2000 domain account
  The ILS server location is published in Active Directory
Otherwise, Phone dialer needs manually configured. On-line help.

## Slide 40: Notes
Create groups for conference security
  ILS has an Access Control List (ACL) limit
  Easier for users to restrict conferences
Multicast over modems is slow
  RAS does not have QOS (yet)
  Phone Dialer uses G.711 (64K audio)
  Bandwidth needs are too high for 56K
  RAS Server can become saturated
H.323 uses G.723 (8K audio)

## Slide 41: For more information
IP Multicast Deployment
  http://www.microsoft.com /windows2000/library/planning /communications/multicaststeps.asp
How Telephony Works:
  http://www.microsoft.com /windows2000/library/howitworks/ communications/telephony
Web Telephony Engine (WTE)
  Fully documented in the Platform SDK
  http://msdn.microsoft.com/isapi/ msdnlib.idc?theURL=/library/psdk/ webte/wteadmin_20md.htm
The Windows 2000 on-line help
Phone Dialer on-line help
Windows 2000 Resource Kit