## Slide 1: Software and System Performance
Thomas J. True, SGI

## Slide 2: Graphics Pipeline
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Notes: Have chosen OpenGL as basis for discussion.
- Available on many computer platforms.
- Easily understood by a general audience.
It's at this level that we will examine the graphics rendering pipeline and how it is implemented by a combination of dedicated graphics hardware and software.
Information presented here for instructional purposes only, not a definitive guide. For more info see spec, SI and MESA.
Slide Graphics: OpenGL Pipeline

## Slide 3: Geometry Path
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Notes: Graphics pipeline composed of a set of paths.
The Geometry Path operates on vertices, colors and normals to produce pixel values which are then drawn into the frame buffer.
(Brief walk through of Geometry Path)
Slide Graphic: Graphics Pipeline with Geometry Path highlighted.

## Slide 4: Image Path
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations

## Slide 5: Texture Path
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Notes: A variation of the DrawPixels path, in the Texture Path image data resulting from the Pixel Transfer Operations is passed to the texel generator rather than the rasterizer.
Texel values are then placed in texture memory to be applied during the texture application stage of the geometry pipeline.

## Slide 6: Readback Path
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Notes: The ReadPixels path is unique in that it works in reverse taking data from the framebuffer and putting it in system memory.
Although the graphics pipeline is primarily designed to render objects into the framebuffer. It is quite common to read rendered images from the framebuffer back into system memory for storage and additional graphics processing.
Pixel data that has been previously rasterized to the framebuffer is read and passed through the same Pixel Transfer Operations and Imaging Subset stages previously described. The data is then packed as specified by the applicatio and placed into system or graphics memory.
Historically, the focus of graphics hardware architecture has been on high-performance geometry processing and pixel fill rates. As a result, the efficient implementation of the read pixels path has been neglected and performs poorly.
Example: AGP
Data transfers to graphics at AGP speeds on both the leading and trailing edges of the clock. However, data can only be read back at half the data rate because the interface on the graphics card can only send data and the leading edges.
Pixel read back can break inherent pipelining and impact performance.

## Slide 7: Implementation
  G - Generate geometric data
  T - Traverse data structures
  X - Transform primitives world to screen
  R - Rasterize primitives to pixels
  D - Display framebuffer on output device
Notes: 5 basic stages introduced in section 2.

## Slide 8: Implementation
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Notes: Overlay 5 basic stages introduced in Section 2 onto OpenGL pipeline.

## Slide 9: Implementation
Four Basic Types.
G-TXRD : all hardware
GT-XRD :
GTX-RD :
GTXR-D : all software
Notes: <number>
<footer>
<header>
<date/time>
1) all hardware (including the T- often a display-list cache in opengl parlance)
2) xf & rast hw
3) raster ops on hw
4) etc.
- note not all work from a phase done in hardware, but there exist some functionality in hw.
- example, do texture, but not fog.

## Slide 10: Implementation: GTXR-D
CPU
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations

## Slide 11: Implementation: GTXR-D
CPU Does Everything!

## Slide 12: Implementation: GTX-RD
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Rendering
Engine
CPU

## Slide 13: Implementation: GTX-RD
Screen space operations performed by one or more rendering engines within graphics subsystem.
Object-space to screen-space transforms and lighting performed by host CPU.

## Slide 14: Implementation: GT-XRD
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Rendering
Engine
CPU
Transform
Engine

## Slide 15: Implementation: GT-XRD
Screen space operations performed by one or more rendering engines within graphics subsystem.
Transforms and lighting performed by one or more geometry engines with graphics subsystem.

## Slide 16: A Delicate Balance
Notes: Graphics performance a delicate balance of hardware and software used to implement the graphics pipeline.
To achieve this balance, an understanding of the graphics pipeline and the underlying system hardware and software which implements is required.
Has become more important as graphics pipeline implemented in dedicated hardware.
This section will examine the hardware side of the equation.
Slide graphics: A balance with Performance in the middle
and software and hardware icons on either side.

## Slide 17: Tuning Process
Quantify
System Evaluation
Graphics Analysis
Bottleneck Elimination

## Slide 18: Quantify
Characterize
  Application Space
  Primitive Types
  Primitive Counts
  Rendering Characteristics
  Frame Rate
CAL

## Slide 19: Quantify
Compare

## Slide 20: System Evaluation
Physical memory.
Disk bandwidth.
Display configuration.
Network characteristics.

## Slide 21: Graphics Analysis
Ideal Performance
  Keep graphics pipeline full.
  100% CPU utilization running application code.
  100% graphics utilization.

## Slide 22: Graphics Analysis Graphics Bound
Acme Electronics
0
100
50
30
10
40
20
90
80
70
60
0
100
50
30
10
40
20
90
80
70
60

## Slide 23: Graphics Analysis Graphics Bound
Graphics subsystem processes data slower than CPU can feed it.
Graphics subsystem issues an interrupt which causes the CPU to stall.
Data processing within application stops until graphics subsystem can again accept data.

## Slide 24: Graphics Analysis Graphics Bound
Geometry Limited
  Limited by the rate at which vertices can be transformed and clipped.
Fill Limited
  Limited by the rate at which transformed vertices can be rasterized.
CAL

## Slide 25: Graphics Analysis CPU Bound
Acme Electronics
0
100
50
30
10
40
20
90
80
70
60
0
100
50
30
10
40
20
90
80
70
60

## Slide 26: Graphics Analysis CPU Bound
CPU at 100% utilization but can’t feed graphics fast enough.
Graphics subsystem at less than 100% utilization.
All CPU cycles consumed by data processing.

## Slide 27: Graphics Analysis
Determination Techniques
  Remove graphics API calls.
  Shrink graphics window.
  Reduce geometry processing requirements.
  Use system monitoring tool.
CAL

## Slide 28: Graphics Analysis
Start
Remove graphics API calls
Graphics Performance Problem
Graphics bound:?
Performance Problem Not Graphics
Graphics bound: fill limited
Graphics bound: geometry limited
Remove rendering calls
Fallen off fast path
Shrink graphics window
Reduce geometry load
Use system monitoring tool
Excessive or unexpected CPU activity
= frame rate increase
= no change in frame rate
CAL

## Slide 29: Graphics Analysis: GTXR-D (aka Dumb Frame Buffer)
CPU
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations

## Slide 30: Graphics Analysis: GTXR-D (aka Dumb Frame Buffer)
CPU does everything.
Typically CPU bound.
To remedy, buy a “real” graphics board.

## Slide 31: Graphics Analysis: GTX-RD
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Rendering
Engine
CPU

## Slide 32: Graphics Analysis: GTX-RD
Screen space operations performed by graphics.
Object-space to screen-space transform on host.
Can easily become CPU bound.
  “Roughly 100 single-precision floating point operations are required to transform, light, clip test, project and map an object-space vertex to screen-space.” - K. Akeley & T. Jermoluk
Beware of fast-path and slow-path issues.

## Slide 33: Graphics Analysis: GTX-RD
If Graphics Bound:
  Reduce per-pixel operations.
  Reduce depth complexity.
  Use native-format data.

## Slide 34: Graphics Analysis: GTX-RD
If CPU Bound:
  Reduce scene complexity.
  Use more efficient graphics algorithms.

## Slide 35: Graphics Analysis: GT-XRD
Model View
Transform
Per-Vertex Operations
Per-Fragment Operations
Pack/Unpack
Pixels
Texture
Memory
Rasterization
Primitive
Assembly
Pixel Transfer
Operations
Rendering
Engine
CPU
Transform
Engine

## Slide 36: Graphics Analysis: GT-XRD
Transformations, lighting and rasterization performed by graphics.
Can be CPU or graphics bound.
Beware of fast-path and slow-path issues.
Subject to host bandwidth limitations.

## Slide 37: Graphics Analysis: GT-XRD
If Graphics Bound:
  Move lighting back to CPU.
  Use native data formats within application.
  Use display lists or vertex arrays.
  Use less expensive lighting modes.

## Slide 38: Graphics Analysis: GT-XRD
If CPU Bound:
  Move lighting from CPU to graphics.
  Do matrix operations in graphics hardware.
  Profile in search of computational performance issues.

## Slide 39: Bottleneck Elimination

## Slide 40: Bottleneck Elimination
Bottlenecks
  Understanding, crucial to effective tuning.
  Will always exist, tune to balance.
  Not always a bad thing.

## Slide 41: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.
Notes: Image data that is not in a format native to the graphics hardware must be repackaged by the graphics software driver before it can be rendered by the graphics subsystem.
Example: BGRA -> RGBA

## Slide 42: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.
Notes: Graphics subsystem is a state machine set to render a particular primitive according to the current settings of the machine.
Changing state forces a pipeline revalidation.
As a result, changing state unnecessarily adds unneeded rendering overhead.
Avoid state changes by organizing primitives so that those with similiar if not identical characteristics are rendered sequentially.
Avoid redundant state calls by cacheing important state information within the application.

## Slide 43: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.
Notes: Graphics pipeline is optimized to receive data and attribute information from the application and render according to the current state settings.
As a result, querying the pipeline for state information breaks the inherent pipelining within the graphics subsystem and can cause the rendering pipeline to stall.
Cache important state information within the application.

## Slide 44: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.

## Slide 45: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.
Notes: Using lighting model characteristics which are unnecessary adds unneeded complexity to the lighting model and geometry processing required to render a scene.
Verify that all lighting state is required for the overall visual quality of the scene.
Example: Local Viewer
Requires the calculation of the angle between the viewer and each object in the scene. With an infinite viewer, this angle is not used producing slightly less realistic results but at a reduced computational cost.
Example: Two-Sided Lighting
Requires lighting calculations to be performed for both front facing and back facing polygons.
Be aware however that to use one-sided lighting effectively, that all normals must be consisten with respect to the geometry. In other words, all normals must point either "out" or "in."
Example: Direct/Infinite vs Local lights
Using direct/infinite lights rather than local lights removes the per-vertex calculation of the attenuation factor in the lighting equation.
Avoid the recalculation of normals within the graphics subsystem by ensuring that all normals are normalized within the application before specification to the graphics subsystem.
Rasterization operations which are not required for visual clarity add unnecessary rendering overhead.
Disable per-fragment operations when they are not required.
Example: Depth Testing
In a visual simulation application, draw background objects such as the sky and ground with the depth buffer disabled, then enable the depth test for foreground objects such as mountains, trees, buildings, etc.

## Slide 46: Bottleneck Elimination Graphics
Use native image formats.
Remove excessive state changes.
Avoid pipeline queries.
Use texture cache efficiently.
Disable unnecessary rendering features.
Decrease scene complexity.
Notes: Depth complexity is the number of times that each pixel is filled.
Reduce depth complexity by culling out unseen or insignificant geometry. Roger will discuss culling in more detail later in the course.

## Slide 47: Bottleneck Elimination Code and Language
Reduce API call overhead.
Use native data types.
Beware of contention for a single shared resource.
Avoid application bottlenecks in non-graphics code.

## Slide 48: API Function Call Overhead
Independent Triangles
(XYZW + RGBA + XYZ + STR) * 9 vertices: 36 function calls
Triangle Strips
(XYZW + RGBA + XYZ + STR) * 5 vertices: 20 function calls
Vertex Array
5 function calls
Display List
1 function call
Notes: Reduce API call overhead.
Macros OK for application code, but not a solution for graphics API calls.
Want to maximize work performed over the cost of entering a function while at the same time maximizing the work performed in a graphics state.
Accomplish this by using display lists, vertex arrays, and stripped primitives.
Example:
Worst case: 4 function calls/vertex
Independent Triangles: 36 function calls
Triangle Strips: 20 function calls
Vertex Array: 5 function calls (could be 2)
Display List: 1 function call (although caveats)

## Slide 49: Bottleneck Elimination Code and Language
Reduce API call overhead.
Use native data types.
Beware of contention for a single shared resource.
Avoid application bottlenecks in non-graphics code.

## Slide 50: Data Types
draw()
{
float x1 = -0.5;
float x2 = 0.5;
float y1 = -0.5;
float y2 = 0.5;
glClear (GL_COLOR_BUFFER_BIT | GL_DEPTH_BUFFER_BIT);
glBegin(GL_QUADS);
glVertex2f(x1, y1);
glVertex2f(x1, y2);
glVertex2f(x2, y2);
glVertex2f(x2, y1);
glEnd();
glXSwapBuffers(dpy, win);
}
33: glVertex2f(x1, y1);
mov esi,esp
mov eax,dword ptr [ebp-0Ch]
push eax
mov ecx,dword ptr [ebp-4]
push ecx
call dword ptr [__imp__glVertex2f@8 (0042b478)]
34: glVertex2f(x1, y2);
mov esi,esp
mov edx,dword ptr [ebp-10h]
push edx
mov eax,dword ptr [ebp-4]
push eax
call dword ptr [__imp__glVertex2f@8 (0042b478)]
Notes: Pass graphics data to API using native data types.
Example: doubles -> floats
In the case of an API expecting vertex data as floats,
data that must be passed in as doubles must be converted to floats by code executing on the host CPU.

## Slide 51: Data Types
draw()
{
double x1 = -0.5;
double x2 = 0.5;
double y1 = -0.5;
double y2 = 0.5;
glClear (GL_COLOR_BUFFER_BIT | GL_DEPTH_BUFFER_BIT);
glBegin(GL_QUADS);
glVertex2f(x1, y1);
glVertex2f(x1, y2);
glVertex2f(x2, y2);
glVertex2f(x2, y1);
glEnd();
glXSwapBuffers(dpy, win);
}
33: glVertex2f(x1, y1);
fld qword ptr [ebp-18h]
fst dword ptr [ebp-24h]
mov esi,esp
push ecx
fstp dword ptr [esp]
fld qword ptr [ebp-8]
fst dword ptr [ebp-28h]
push ecx
fstp dword ptr [esp]
call dword ptr [__imp__glVertex2f@8 (0042b478)]
34: glVertex2f(x1, y2);
fld qword ptr [ebp-20h]
fst dword ptr [ebp-2Ch]
mov esi,esp
push ecx
fstp dword ptr [esp]
fld qword ptr [ebp-8]
fst dword ptr [ebp-30h]
push ecx
0fstp dword ptr [esp]
dword ptr [__imp__glVertex2f@8 (0042b478)]
Notes: Pass graphics data to API using native data types.
Example: doubles -> floats
In the case of an API expecting vertex data as floats,
data that must be passed in as doubles must be converted to floats by code executing on the host CPU.

## Slide 52: Bottleneck Elimination Code and Language
Reduce API call overhead.
Use native data types.
Beware of contention for a single shared resource.
Avoid application bottlenecks in non-graphics code.
Notes: Architect application so that:
1. Multiple rendering threads not waiting for a single graphics context.
2. Multiple graphics contexts not waiting for access to a single graphics device.

## Slide 53: Bottleneck Elimination Code and Language
Reduce API call overhead.
Use native data types.
Beware of contention for a single shared resource.
Avoid application bottlenecks in non-graphics code.
Notes: Bottlenecks can also be found in non-graphics part of application.
Profile the application to find these types of bottlenecks.
Keith will describe profiling techniques after the break.

## Slide 54: Bottleneck Elimination Memory
Don’t allocate memory in rendering loop.
Avoid copying and repackaging of graphics data.
Organize graphics data to maximize bandwidth and avoid fragmentation.
Notes: Memory allocation requires a system call and an expensive context switch from user mode to system mode.
As a result, allocating memory within a rendering loop can cause the graphics subsystem to stall waiting for the system call to complete.
Allocate memory before entering the graphics rendering loop.

## Slide 55: Bottleneck Elimination Memory
Don’t allocate memory in rendering loop.
Avoid copying and repackaging of graphics data.
Organize graphics data to maximize bandwidth and avoid fragmentation.
Notes: Don't make local copies of data.

## Slide 56: Bottleneck Elimination Memory
Don’t allocate memory in rendering loop.
Avoid copying and repackaging of graphics data.
Organize graphics data to maximize bandwidth and avoid fragmentation.

## Slide 57: Bandwidth and Fragmentation
Independent Triangles
9 vertices: 504 bytes
Triangle Strip
5 vertices: 280 bytes
Vertex Array
5 vertices: 280 bytes
Vertex = RGBA+XYZW+XYZ+STR = 56 bytes
Notes: Each transfer of data from memory to graphics requires overhead and system bus traffic.
Amortize this overhead and maximize data bandwidth by organizing per-vertex data to use vertex arrays.
Vertex array code is optimized to efficiently transfer data to the graphics subsystem.
Sparsely packed data cuases memory fragmentation and as a result, poor cache behaviour.
Avoid memory fragmentation by allocating memory from a pre-allocated pool. This reduces expensive memory paging operations when traversing graphics data.
Example:
Worst case: 56 bytes/vertex
So, as independent triangles: 504 bytes
Win #1, triangle strip 280 bytes (224 byte saving)
Win #2, vertex array - doesn't reduce memory requirements by eliminates fragmentation.

## Slide 58: Conclusion
Rendering
Engine
Transform
Engine
CPU
Implementation a Team Effort

## Slide 59: Conclusion
Quantify
System Evaluation
Graphics Analysis
Bottleneck Elimination
Tuning a Four Step Process
Notes: Performance Tuning is an Iterative Process

## Slide 60: Conclusion
It’s all about balance!